## Slide 1
CSCE 5520
Wireless Networks and Protocols Wireless Challenges

## Slide 2: Outline
Challenges in Wireless Networking
RF introduction
» A cartoon view
» Communication
» Time versus frequency view
Modulation and multiplexing
Channel capacity
Antennas and signal propagation
Modulation
Diversity and coding
OFDM

## Slide 3: Why Use Wireless?
There are no wires!
Has several significant advantages:
Supports mobile users
» Move around office, campus, city, … - users get hooked
» Remote control devices (TV, garage door, ..)
» Cordless phones, cell phones, ..
» WiFi, GPRS, Bluetooth, …
No need to install and maintain wires
» Reduces cost – important in offices, hotels, …
» Simplifies deployment – important in homes, hotspots, …

## Slide 4: What is Hard about Wireless?
There are no wires!
In wired networks links are constant, reliable and physically isolated
» A 1 GBps Ethernet always has the same properties
» Not true for “54 Mbps” 802.11a and definitely not for “6 Gbps” 802.11ac
In wireless networks links are variable, error- prone
» Link properties can be extremely dynamic
» For mobile devices they also differ across locations

## Slide 5: Wireless is a shared medium
In wired communication, signals are contained in a conductor
» Copper or fiber
» Guides energy to destination
» Protects signal from external signals
Wireless communication uses broadcasting over the shared ether
» Energy is distributed in space
» Signal must compete with many other signals in same frequency band
Bob
Mary

## Slide 6: Attenuation and Errors
In wired networks error rate 10-10 or less
» Wireless networks are far from that target
Signal attenuates with distance and is affected by noise and competing signals
Obstacles further attenuate the signal
Probability of a successful reception depends on the “signal to interference and noise ratio”
- the SINR
More details later in the course
Bob
Mary

## Slide 7: How Do We Increase Network Capacity?
Easy to do in wired networks: simply add wires
» Fiber is especially attractive
Adding wireless “links” increases interference.
» Frequency reuse can help … subject to spatial limitations
» Or use different frequencies … subject to frequency limitations
The capacity of the wireless network is fundamentally limited.
Bob
Mary

## Slide 8: Mobility Affects the Link Throughput
Quality of the transmission depends on distance and obstacles blocking the “line of sight” (LOS)
» “Slow fading” – the signal strength changes slowly
Reflections off obstacles combined with mobility can cause “fast fading”
» Very rapid changes in the signal
» More on this later
Hard to predict signal!
Bob
Mary

## Slide 9: How is Wireless Different?
Wired
Physical link properties are fixed and specified in standards
Designed for low error rates and throughput is fixed and known
Datalink layer is simple and optimized for the physical layer
Internet was designed assuming low error rates
Wireless
Physical link properties can change rapidly in unpredictable ways
Error rates vary a lot and throughput is very dynamic
How do you design an efficient datalink protocol?
How well will higher layer protocols work?

## Slide 10: Implications of Variability in Wireless PHY Layer
Wireless datalink protocols must optimize throughput across an unknown and dynamic transmission medium
» Important to understand what causes the changes
Wireless “links” as observed by layers 3-7 will be unavoidably different from wired links
» Variable bandwidth and latency
» Intermittent connectivity
» Must adapt to changes in connectivity and bandwidth
Understanding the physical layer is the key to making wireless work well
» High level intuition is sufficient

## Slide 11: Outline
Challenges in Wireless Networking
RF introduction
» A cartoon view
» Communication
» Time versus frequency view
Modulation and multiplexing
Channel capacity
Antennas and signal propagation
Modulation
Diversity and coding
OFDM

## Slide 12: From Signals to Packets
“Digital” Signal
Analog Signal
Bit Stream
Header/Body Header/Body Header/Body
0 0 1 0 1 1 1 0 0 0 1
Packets
Sender Receiver
01000101010111001010101010111011100000011110101011101010101011010110101
12
Packet Transmission

## Slide 13: RF Introduction
RF = Radio Frequency
» Electromagnetic signal that propagates through “ether”
» Ranges 3 KHz .. 300 GHz
» Or 100 km .. 0.1 cm (wavelength)
Travels at the speed of light
Can take both a time and a frequency view
13

## Slide 14: Cartoon View 1 – A Wave of Energy
Think of it as energy that radiates from an antenna and is picked up by another antenna.
Helps explain properties such as attenuation
» Density of the energy reduces over time, distance
» Signal strength is reduced, error rates go up
Relevance to networking?
» Error rates of “wireless” depend on distance
  Also depends on many properties
» Notion spatial reuse of frequencies
  Basis of cellular and WiFi infrastructures
14

## Slide 15: Cartoon View 2 – Rays of Energy
15
Can also view it as a “ray” that propagates between two points
» Rays can be reflected etc.
» A channel can include multiple “rays” that take different paths – “multi-path” effect
Implications for wireless networks
» We can have provide connectivity without line of sight!
» Receiver can receive multiple copies of the signal, which leads to signal distortion
» Combined with mobility, it also leads to fast fading

## Slide 16: (Not So) Cartoon View 3 – Electro-magnetic Signal
16
Signal that propagates and changes over time with a certain frequency and has an amplitude and phase
» Think: sine wave
Relevance to networking?
» The sender can change the properties of the EM signal over time to convey information
» Receivers can observe these changes and extract the information

## Slide 17: Dealing With Bit Errors
18
Wireless vs. wired links
  Wired: most loss is due to congestion
  Wireless: higher, time-varying bit-error ate
Dealing with high bit-error rates
  Sender could increase transmission power
    Requires more energy (bad for battery-powered hosts)
    Creates more interference with other senders
  Stronger error detection and recovery
    More powerful error detection codes
    Link-layer retransmission of corrupted frames

## Slide 18: Communication
Time (point in space)
Space (snapshot in time)
Sender changes signal in agree upon way and receiver interprets the changes
» “Modulation” and “Demodulation”
Problem: the signal gets distorted on “channel”
» Makes it harder for receiver to interpret changes
Transmitter
Received Signal
Remember: Cartoon view

## Slide 19: Sine Wave Parameters
General sine wave
» s(t ) = A Sin(2πft + θ)
A = Amplitude, f = Frequency,
θ = Phase, Period T = 1/f,
Frequency is measured in Cycles/sec or Hertz

## Slide 20: Sine Wave Parameters
  A = 1, f = 1 Hz, θ = 0; thus T = 1s
  Reduced peak amplitude; A=0.5
  Increased frequency; f = 2, thus T = ½
  Phase shift;  θ = ¼ radians (45 degrees)
note: 2 radians = 360° = 1 period

## Slide 21: Phase
Phase is measurement of the sine wave, and it indicates where the wave is in its cycle. It is measured in degrees (0°-360°) or radians (0-2π) and is denoted with the Greek symbol Phi (ϕ).

## Slide 22: Amplitude
Amplitude indicates how far the wave deviates from its position of rest.

## Slide 23: Wavelength
Wavelength is the distance between identical points (adjacent crests) in the adjacent cycles of a waveform signal propagated in space or along a wire.
Wavelength is inversely related to frequency, which refers to the number of wave cycles per second. The higher the frequency of the signal, the shorter the wavelength.
Wavelength = λ
Assuming signal velocity v
    λ= vT
    λf = v
c = 3×108 m/s(speed of light in free space) = 300 m/μs

## Slide 24: Example
Frequency = 2.5 GHz
  λ = c/f
  = 300m/μs

## Slide 25: Key Idea of Wireless Communication
The sender sends an EM signal and changes its properties over time
» Changes reflect a digital signal, e.g., binary or multi-valued signal
» Can change amplitude, phase, frequency, or a combination
Receiver learns the digital signal by observing how the received signal changes
» Note that signal is no longer a simple sine wave or even a periodic signal

## Slide 26: Outline
Challenges in Wireless Networking
RF introduction
» A cartoon view
» Communication
» Time versus frequency view
Modulation and multiplexing
Channel capacity
Antennas and signal propagation
Modulation
Diversity and coding
OFDM

## Slide 27: Challenge
Wireless network designers need more precise information about the performance of wireless “links”
» Can the receiver always decode the signal?
» How many Kbit, Mbit, Gbit per second?
» Does the physical environment, distance, mobility, weather, season, the color of my shirt, etc. matter?
We need a more formal way of reasoning about wireless communication:
Represent the signal in the frequency domain!

## Slide 28: Time Domain View: Periodic versus Aperiodic Signals
Periodic signal - analog or digital signal pattern that repeats over time
»
s(t +T ) = s(t )
– where T is the period of the signal
» Allows us to take a frequency view – important to understand wireless challenges and solutions
Aperiodic signal - analog or digital signal pattern that doesn't repeat over time
» Hard to analyze
Can “make” an aperiodic signal periodic by taking a time slice T and repeating it
» Often what we do implicitly

## Slide 29: common periodic waveforms

## Slide 30: Key Property of Periodic EM Signals
Any electromagnetic signal can be shown to consist of a collection of periodic analog signals (sine waves) at different amplitudes, frequencies, and phases
The period of the total signal is equal to the period of the fundamental frequency
» All other frequencies are an integer multiple of the fundamental frequency
There is a strong relationship between the “shape” of the signal in the time and frequency domain

## Slide 31: Analog vs. Digital Communication System

## Slide 32: Wireless Communication System

## Slide 33: Wireless Communication System

## Slide 34: Coding Terminology
Notes: A pulse in signal processing is a rapid, transient change in the amplitude of a signal from a baseline value to a higher or lower value, followed by a rapid return to the baseline value
It is the unit for symbol rate or modulation rate in symbols per second or pulses per second. It is the number of distinct symbol changes (signaling events) made to the transmission medium per second in a digitally modulated signal or a bd rate line code.

## Slide 35: Signal Modulation
Modulation: the process of encoding the information from a message source in a manner suitable for transmission
  Amplitude modulation (AM): change the strength of the carrier based on information
    High values -> stronger signal
  Frequency (FM) and phase modulation (PM): change the frequency or phase of the signal
    Frequency or Phase shift keying
Digital versions are also called “shift keying”
  Amplitude (ASK), Frequency (FSK), Phase (PSK) Shift Keying

## Slide 36: Signal Modulation

## Slide 37: Signal Modulation

## Slide 38: Signal Modulation

## Slide 39: Signal Modulation

## Slide 40: Signal Modulation

## Slide 41: Signal Modulation

## Slide 42: Signal Modulation

## Slide 43: Signal Modulation

## Slide 44: Signal Modulation

## Slide 45: Signal Modulation

## Slide 46: Signal Modulation

## Slide 47: Signal Modulation

## Slide 48: QAM

## Slide 49: Example

## Slide 50: BPSK Modulation

## Slide 51: BPSK Modulation

## Slide 52: BPSK Modulation

## Slide 53: BPSK Modulation

## Slide 54: BPSK Modulation

## Slide 55: BPSK Modulation

## Slide 56: Signal Modulation

## Slide 57: QAMs

## Slide 59: Numeric example
For a communication system, the 4 bits are encoded per symbol and four symbols are transmitted per second. Compute the bit rate of the system
Multiple bits are encoded per symbol to increase the bit rate
By substituting the known values, we can find the bit rate of the system to be 16 bits/second.

## Slide 60: Noise
Circuit Components and wireless channel add noise to the wireless signal.
v(t) is Additive White Gaussian Noise (AWGN)
High noise is bad -> Cannot decode Bits correctly Low noise is good -> Can decode Bits correctly
Signal-to-Noise Ratio (SNR)

## Slide 61: Noise
The noise level indicates the amount of background noise in your environment.
  If the noise level is too high, it can result in degraded strength and performance for your wireless signal strength.
  Noise level is measured in -dBm format (0 to -100). This is the power ratio in decibels (dB) of the measured power referenced to one milliwatt.
  The closer the value to 0, the greater the noise level.
  Negative values indicate less background noise. For example, -96dBm is a lower noise level than -20dBm.

## Slide 62: Decibel (dB)
The decibel (dB) is a unit used to express the ratio of powers of sound pressure, signal strength or other things on logarithmic scale.
The decibel is a relative unit of measurement equal to one tenth of a bel (B), invited by Bell Labs and named after Alexander Graham Bell.
        Decibel = 10 * log10 (Po/Pi) dB
  Where Po is output power and Pi is an input power

## Slide 63: Decibel (dB)
Note decibel is a relative value
  decibel-watt (db) = power relative to 1W
  Decibel-milliwatt(dBm) = power relative to 1 milliwatt
The logarithmic scale is used to is to avoid dealing with very high and very low numbers, meaning the ratio. Using decibels is easy to work with
  For example:
    A power of ratio of 1,000,000 (1million) can be expressed by 60dB
    A power of ratio of 0.000001 can be expressed by -60dB
    A power of ratio of 1,000,000,000,000,000 (1quadrillion) can be expressed by 150dB
    A power of ratio of 0.000000000000000 1 can be expressed by -150dB

## Slide 64: Signal to Noise Ratio
Ratio of the power in a signal to the power contained in the noise that’s present at a particular point in the transmission
  Typically measured at a receiver
Signal-to-noise ratio (SNR, or S/N)
SNR is a essential parameter that shows signal quality
  high SNR means a high-quality signal, low number of required intermediate repeaters
  A low SNR means low quality signal, may require further signal processing to recover original signal
We typically measure SNR in db scale

## Slide 65: Channel Capacity
Channel capacity is a maximum information rate that a channel can transmit. It is measured in bits per second (bps). Channel capacity is a rough value as measuring takes into account only the whole amount of data transferred but leaves out of account communication quality.
Bandwidth can be considered as a subset of channel capacity term. When bandwidth is measured, the maximum volume of information that can be accurately transferred per unit of time is taken into account.
For example, channel capacity may be very high, but low signal quality would make bandwidth low as well.

## Slide 66: Concepts related to Channel Capacity
Data rate - rate at which data can be communicated (bps)
Bandwidth - the bandwidth of the transmitted signal as constrained by the transmitter and the nature of the transmission medium (Hertz)
Noise - average level of noise over the communications path
Error rate - rate at which errors occur
  Error = transmit 1 and receive 0; transmit 0 and receive 1
    Implying the probability of one bit error
    Example : Bit error rate of 10-3 means probability of a single bit flipped, or in other words, in every 1000 bit, one bit error is found

## Slide 67: Concepts related to Channel Capacity
Channel Capacity
  Channel can be thought as a pipe, which certain maximum water (bit) can flow (propagate) through
  Channel capacity infer the maximum number of bit per unit time that can transmitted through a channel with a very small bit error rate.
Wireless channel capacity
  Transmitting digital data using analog signal
  Shannon Channel Capacity
    Upper bound channel capacity, with present of noise regardless channel coding scheme,
    Never being reached in practice
Where C is the channel capacity (in bit/second), B is the channel bandwidth (Hz), and SNR is signal to noise ratio quantity (It is in linear scale)
        C = B log 2(1+SNR)

## Slide 68: Shannon’s Theorem

## Slide 69: The Nyquist Limit
A noiseless channel of bandwidth B can at most transmit a binary signal at a capacity 2B
  » e.g., a 3000 Hz channel can transmit data at a rate of at most 6000 bits/second
  » Assumes binary amplitude encoding
For M levels: C = 2B log2 M
  » M discrete signal levels
More aggressive encoding can increase the actual channel bandwidth
  » Example: modems
Factors such as noise can reduce the capacity

## Slide 70: Example

## Slide 71: Example

## Slide 72: Multiplexing
Capacity of the transmission medium usually exceeds the capacity required for a single signal
Multiplexing - carrying multiple signals on a single medium
» More efficient use of transmission medium
A must for wireless – spectrum is huge!
» Signals must differ in frequency (spectrum), time, or space

## Slide 73: Multiplexing Techniques
Frequency-division multiplexing (FDM)
» divide the capacity in the frequency domain
Time-division multiplexing (TDM)
» Divide the capacity in the time domain
» Fixed or variable length time slices

## Slide 74: Multiple Users Can Share the Ether
Different users use Different carrier frequencies
Frequency

## Slide 75: Frequency versus Time-division Multiplexing
With frequency-division
multiplexing different users use
different parts of the frequency spectrum.
» I.e. each user can send all the time at reduced rate
» Example: roommates
» Hardware is slightly more expensive and is less efficient use of spectrum
With time-division multiplexing
different users send at different times.
» I.e. each user can sent at full speed some of the time
» Example: a time-share condo
» Drawback is that there is some
transition time between slots;
becomes more of an issue with longer propagation times
The two solutions can be combined.
Frequency
Slot |  |  | Frame |  |  | 
Time
Frequency Bands

## Slide 76: Frequency Reuse in Space
Frequencies can be reused in space
» Distance must be large enough
» Example: radio stations
Basis for “cellular” network architecture
Set of “base stations” connected to the wired network support set of nearby clients
» Star topology in each circle
» Cell phones, 802.11, …