## Slide 1: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols

## Slide 2: 4G/5G cellular networks
the solution for wide-area mobile Internet
widespread deployment/use:
  more mobile-broadband-connected devices than fixed-broadband-connected devices devices (5-1 in 2019)!
  4G availability: 97% of time in Korea (90% in US)
transmission rates up to 100’s Mbps
technical standards: 3rd Generation Partnership Project (3GPP)
  wwww.3gpp.org
  4G: Long-Term Evolution (LTE)standard

## Slide 3: 4G/5G cellular networks
similarities to wired Internet
edge/core distinction, but both below to same carrier
global cellular network: a network of networks
widespread use of protocols we’ve studied: HTTP, DNS, TCP, UDP, IP, NAT, separation of data/control planes, SDN, Ethernet, tunneling
interconnected to wired Internet
differences from wired Internet
different wireless link layer
mobility as a 1st class service
user “identity” (via SIM card)
business model: users subscribe to a cellular provider
  strong notion of “home network” versus roaming on visited nets
  global access, with authentication infrastructure, and inter-carrier settlements

## Slide 4: Elements of 4G LTE architecture
Mobile device
(UE)
Base station
(eNode-B)
radio access
network
all-IP Enhanced Packet Core (EPC)
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
to
Internet
…
Mobile device:
smartphone, tablet, laptop, IoT, ... with 4G LTE radio
64-bit International Mobile Subscriber Identity (IMSI), stored on SIM (Subscriber Identity Module) card
LTE jargon: User Equipment (UE)

## Slide 5: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Base station:
at “edge” of carrier’s network
manages wireless radio resources, mobile devices in its coverage area (“cell”)
coordinates device authentication with other elements
similar to WiFi AP but:
  active role in user mobility
  coordinates with nearly base stations to optimize radio use
LTE jargon: eNode-B

## Slide 6: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Home Subscriber Service
stores info about mobile devices for which the HSS’s network is their “home network”
works with MME in device authentication

## Slide 7: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Serving Gateway (S-GW), PDN Gateway (P-GW)
lie on data path from mobile to/from Internet
P-GW
  gateway to mobile cellular network
  Looks like nay other internet gateway router
  provides NAT services
other routers:
  extensive use of tunneling

## Slide 8: Elements of 4G LTE architecture
Mobility Management Entity (MME)
Serving Gateway (S-GW)
Home Subscriber Service (HSS)
PDN gateway (P-GW)
…
to
Internet
Mobile device
(UE)
Base station
(eNode-B)
Mobility Management Entity
device authentication (device-to-network, network-to-device) coordinated with mobile home network HSS
mobile device management:
  device handover between cells
  tracking/paging device location
path (tunneling) setup from mobile device to P-GW

## Slide 9: LTE: data plane control plane separation
control plane
new protocols for mobility management , security, authentication (later)
MME
HSS
base station
P-GW
S-GW
base station
P-GW
S-GW
data plane
new protocols at link, physical layers
IP tunnels
extensive use of tunneling to facilitate mobility

## Slide 10: LTE data plane protocol stack: first hop
IP
Packet Data
Convergence
Radio Link
Medium Access
Physical
data
plane
P-GW
S-GW
Application
Transport
IP
Packet Data
Convergence
Radio Link
Medium Access
Physical
Link
base station
LTE link layer protocols:
Packet Data Convergence: header compression, encryption
Radio Link Control (RLC) Protocol: fragmentation/reassembly, reliable data transfer
Medium Access: requesting, use of radio transmission slots

## Slide 11: LTE data plane protocol stack: first hop
IP
Packet Data
Convergence
Radio Link
Medium Access
Physical
Application
Transport
IP
Packet Data
Convergence
Radio Link
Medium Access
Physical
Link
base station
LTE radio access network:
downstream channel: FDM, TDM within frequency channel (OFDM - orthogonal frequency division multiplexing)
  “orthogonal”: minimal interference between channels
  upstream: FDM, TDM similar to OFDM
each active mobile device allocated two or more 0.5 ms time slots over 12 frequencies
  scheduling algorithm not standardized – up to operator
  100’s Mbps per device possible

## Slide 12: LTE data plane protocol stack: packet core
IP
Packet Data
Convergence
Radio Link
Medium Access
Physical
GTP-U
UDP
IP
link
Physical
GTP-U
UDP
IP
link
Physical
GTP-U
UDP
IP
link
Physical
P-GW
S-GW
base station
\
tunneling:
mobile datagram encapsulated using GPRS Tunneling Protocol (GTP), sent inside UDP datagram to S-GW
S-GW re-tunnels datagrams to P-GW
supporting mobility: only tunneling endpoints change when mobile user moves

## Slide 13: LTE data plane: associating with a BS
data
plane
P-GW
S-GW
base station
BS broadcasts primary synch signal every 5 ms on all frequencies
BSs from multiple carriers may be broadcasting synch signals
1
mobile finds a primary synch signal, then locates 2nd synch signal on this freq.
mobile then finds info broadcast by BS: channel bandwidth, configurations; BS’s cellular carrier info
mobile may get info from multiple base stations, multiple cellular networks
2
mobile selects which BS to associate with (e.g., preference for home carrier)
3
more steps still needed to authenticate, establish state, set up data plane
4
1
2
3

## Slide 14: LTE mobiles: sleep modes
data
plane
ZZZZ...
as in WiFi, Bluetooth: LTE mobile may put radio to “sleep” to conserve battery:
light sleep: after 100’s msec of inactivity
  wake up periodically (100’s msec) to check for downstream transmissions
deep sleep: after 5-10 secs of inactivity
  mobile may change cells while deep sleeping – need to re-establish association

## Slide 15: Global cellular network: a network of IP networks
…
visited mobile
carrier network
…
public Internet
and
inter-carrier IPX
…
P-GW
P-GW
home mobile
carrier network
Home
Subscriber
Server
in home network
roaming in visited network
SIM card: global identify info in home network
all IP:
carriers interconnect with each other, and public internet at exchange points
legacy 2G, 3G: not all IP, handled otherwise
home network HSS:
identify & services info, while in home network and roaming

## Slide 16: On to 5G!
goal: 10x increase in peak bitrate, 10x decrease in latency, 100x increase in traffic capacity over 4G
5G NR (new radio):
  two frequency bands: FR1 (450 MHz–6 GHz) and FR2 (24 GHz–52 GHz): millimeter wave frequencies
  not backwards-compatible with 4G
  MIMO: multiple directional antennae
millimeter wave frequencies: much higher data rates, but over shorter distances
  pico-cells: cells diameters: 10-100 m
  massive, dense deployment of new base stations required

## Slide 17: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols

## Slide 18: What is mobility?
spectrum of mobility, from the network perspective:
no mobility
high mobility
device moves
between networks, but
powers down
while moving
device moves within same AP in
one provider
network
device moves
among multiple
provider networks,
while maintaining
ongoing connections
device moves among APs in
one provider
network
We’re interested in these!

## Slide 19: Mobility approaches
let network (routers) handle it:
  routers advertise well-known name, address (e.g., permanent 32-bit IP address), or number (e.g., cell #) of visiting mobile node via usual routing table exchange
  Internet routing could do this already with no changes! Routing tables indicate where each mobile located via longest prefix match!

## Slide 20: Mobility approaches
let network (routers) handle it:
  routers advertise well-known name, address (e.g., permanent 32-bit IP address), or number (e.g., cell #) of visiting mobile node via usual routing table exchange
  Internet routing could do this already with no changes! Routing tables indicate where each mobile located via longest prefix match!
let end-systems handle it: functionality at the “edge”
  indirect routing: communication from correspondent to mobile goes through home network, then forwarded to remote mobile
  direct routing: correspondent gets foreign address of mobile, send directly to mobile
not
scalable
to billions of
mobiles

## Slide 21: Contacting a mobile friend:
search all phone books?
expect her to let you know where he/she is?
I wonder where Alice moved to?
Consider friend frequently changing locations, how do you find him/her?
call his/her parents?
Facebook!
The importance of having a “home”:
a definitive source of information about you
a place where people can find out where you are

## Slide 22: Home network, visited network: 4G/5G
…
visited mobile
carrier network
…
public Internet
and
inter-carrier IPX
…
P-GW
P-GW
home mobile
carrier network
Home
Subscriber
Server
in home network
roaming in visited network
SIM card: global identify info including home network
home network:
(paid) service plan with cellular provider, e.g., Verizon, Orange
home network HSS stores identify & services info
visited network:
any network other than your home network
service agreement with other networks: to provide access to visiting mobile

## Slide 23: Home network, visited network: ISP/WiFi
…
…
public Internet
…
authentication
access
server
attach
attach
authentication
access
server
ISP/WiFi: no notion of global “home”
credentials from ISP (e.g., username, password) stored on device or with user
ISPs may have national, international presence
different networks: different credentials
  some exceptions (e.g., eduroam)
  architectures exist (mobile IP) for 4G-like mobility, but not used

## Slide 24: Home network, visited network: generic
Home gateway
Home Network
  e.g.,: 128.119/16
Home network gateway
Permanent IP:
128.119.40.186
IMSI
78:4f:43:98:d9:27
Visited network gateway
NAT IP:
10.0.0.99
IMSI
78:4f:43:98:d9:27
public or private Internet
Home
Subscriber
Server
Mobility manager
Mobility manager
Correspondent
Visited Network
e.g.,: 79.129/16

## Slide 25: Registration: home needs to know where you are!
Home gateway
Home network gateway
Permanent IP:
128.119.40.186
IMSI
78:4f:43:98:d9:27
Visited network gateway
NAT IP:
10.0.0.99
IMSI
78:4f:43:98:d9:27
public or private Internet
Home
Subscriber
Server
Mobility manager
Mobility manager
end result:
visited mobility manager knows about mobile
home HSS knows location of mobile
2
visited mobility manager registers mobile’s location with home HSS
mobile associates with visited mobility manager
1
Home Network
  e.g.,: 128.119/16
Visited Network
e.g.,: 79.129/16

## Slide 26: Mobility with indirect routing
Home gateway
Home network gateway
Permanent IP:
128.119.40.186
IMSI
78:4f:43:98:d9:27
Visited network gateway
NAT IP:
10.0.0.99
IMSI
78:4f:43:98:d9:27
public or private Internet
Home
Subscriber
Server
Mobility manager
Mobility manager
Correspondent
1
correspondent uses home address as datagram destination address
home gateway receives datagram, forwards (tunnels) to remote gateway
Home Network
  e.g.,: 128.119/16
Visited Network
e.g.,: 79.129/16
2
3
4a
4b
visited gateway router forwards to mobile
visited gateway router forwards reply to correspondent via home network (4a) or directly (4b)

## Slide 27: Mobility with indirect routing: comments
triangle routing:
  inefficient when correspondent and mobile are in same network
mobile moves among visited networks: transparent to correspondent!
  registers in new visited network
  new visited network registers with home HSS
  datagrams continue to be forwarded from home network to mobile in new network
  on-going (e.g., TCP) connections between correspondent and mobile can be maintained!

## Slide 28: Mobility with direct routing
Home gateway
Permanent IP:
128.119.40.186
IMSI
78:4f:43:98:d9:27
Visited network gateway
NAT IP:
10.0.0.99
IMSI
78:4f:43:98:d9:27
public or private Internet
Home
Subscriber
Server
Mobility manager
Mobility manager
Correspondent
1
correspondent contacts home HSS, gets mobile’s visited network
Home Network
  e.g.,: 128.119/16
Visited Network
e.g.,: 79.129/16
4
visited gateway router forwards to mobile
2
3
Correspondent addresses datagram to visited network address

## Slide 29: Mobility with direct routing: comments
overcomes triangle routing inefficiencies
non-transparent to correspondent: correspondent must get care-of-address from home agent
what if mobile changes visited network?
  can be handled, but with additional complexity

## Slide 30: Chapter 7 outline
Introduction
Wireless
Wireless links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols

## Slide 31: Mobility in 4G networks: major mobility tasks
Mobility manager
Visited network
P-GW
Streaming server
Home
network
Internet
base station
MME
1
2
3
4
Home
Subscriber
Server
S-GW
P-GW
base station association:
covered earlier
mobile provides IMSI – identifying itself, home network
1
control-plane configuration:
MME, home HSS establish control-plane state - mobile is in visited network
2
data-plane configuration:
MME configures forwarding tunnels for mobile
visited, home network establish tunnels from home P-GW to mobile
3
mobile handover:
mobile device changes its point of attachment to visited network
4

## Slide 32: Configuring LTE control-plane elements
Mobility manager
Mobile communicates with local MME via BS control-plane channel
MME uses mobile’s IMSI info to contact mobile’s home HSS
  retrieve authentication, encryption, network service information
  home HHS knows mobile now resident in visited network
BS, mobile select parameters for BS-mobile data-plane radio channel
Visited network
P-GW
Home
network
base station
MME
2
Home
Subscriber
Server
S-GW
P-GW

## Slide 33: Configuring data-plane tunnels for mobile
Mobility manager
P-GW
Streaming server
Internet
base station
MME
Home
Subscriber
Server
S-GW
P-GW
Visited network
Home
network
S-GW to BS tunnel: when mobile changes base stations, simply change endpoint IP address of tunnel
S-GW to home P-GW tunnel: implementation of indirect routing
tunneling via GTP (GPRS tunneling protocol): mobile’s datagram to streaming server encapsulated using GTP inside UDP, inside datagram

## Slide 34: Handover between BSs in same cellular network
P-GW
S-GW
MME
source BS
1
3
2
data path before handover
data path after
handover
1
current (source) BS selects target BS, sends Handover Request message to target BS
2
target BS pre-allocates radio time slots, responds with HR ACK with info for mobile
3
source BS informs mobile of new BS
mobile can now send via new BS - handover looks complete to mobile
4
source BS stops sending datagrams to mobile, instead forwards to new BS (who forwards to mobile over radio channel)
target BS
4

## Slide 35: Handover between BSs in same cellular network
1
6
3
5
5
2
5
target BS informs MME that it is new BS for mobile
MME instructs S-GW to change tunnel endpoint to be (new) target BS
6
target BS ACKs back to source BS: handover complete, source BS can release resources
P-GW
S-GW
MME
source BS
target BS
4
7
7
mobile’s datagrams now flow through new tunnel from target BS to S-GW

## Slide 36: Mobile IP
mobile IP architecture standardized ~20 years ago [RFC 5944]
  long before ubiquitous smartphones, 4G support for Internet protocols
  did not see wide deployment/use
  perhaps WiFi for Internet, and 2G/3G phones for voice were “good enough” at the time
mobile IP architecture:
  indirect routing to node (via home network) using tunnels
  mobile IP home agent: combined roles of 4G HSS and home P-GW
  mobile IP foreign agent: combined roles of 4G MME and S-GW
  protocols for agent discovery in visited network, registration of visited location in home network via ICMP extensions

## Slide 37: Wireless, mobility: impact on higher layer protocols
logically, impact should be minimal …
  best effort service model remains unchanged
  TCP and UDP can (and do) run over wireless, mobile
… but performance-wise:
  packet loss/delay due to bit-errors (discarded packets, delays for link-layer retransmissions), and handover loss
  TCP interprets loss as congestion, will decrease congestion window un-necessarily
  delay impairments for real-time traffic
  bandwidth a scare resource for wireless links

## Slide 38: Chapter 7 summary
Wireless
Wireless Links and network characteristics
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Mobility
Mobility management: principles
Mobility management: practice
  4G/5G networks
  Mobile IP
Mobility: impact on higher-layer protocols