## Slide 1
CSCE 5520:
Wireless Networks and Protocols
1

## Slide 2: Ad Hoc Routing
2
Definition and challenges
Routing:
» Classes: proactive versus reactive routing
» Proactive, table based routing: DSDV
» Reactive routing DSR
» Geographic routing: GPSR
Discussion
Structured as a survey
» But a bit longer since it covers more material

## Slide 3: Ad Hoc Networking
Goal: Communication between wireless nodes
» No infrastructure – network must be self-configuring
It may require multiple hops to reach a destination
» Nodes are traffic sources, sinks and forwarders
3

## Slide 4: Ad Hoc Networking Challenging
4
All the challenges of wireless, and more:
» Decentralized: nobody is in charge – no planning!
» No fixed infrastructure, random network design
» Generic ad hoc can be arbitrarily bad: limited batteries, malicious nodes, high mobility, low density, ..
Precise challenges depend on the application domain, e.g., vehicular networks versus first- responder networks versus sensor networks
» Domain focus typically simplifies the problem
» Most research papers address the complex general case
The big challenge: Routing

## Slide 5: Traditional Routing vs Ad Hoc
Traditional wired network:
» Well-structured
» ~O(N) nodes & links
» All links work equally well
» Sensible topology
» Links are independent
Ad Hoc wireless network
» N2 links - but many stink!
» Topology may be really weird
» Links interfere with each other
» Dynamic link conditions affect link quality unpredictably
– So the topology also changes constantly!
5

## Slide 6: Forwarding Packets is expensive
6

## Slide 7: Ad Hoc Routing
7
Proactive routing: each router maintains a forwarding table listing all destinations
» Uses routing algorithms similar to those in the Internet
» Example: traditional algorithms with wireless metrics
Reactive routing: only find a path when you need it
» Avoids the overhead of periodically executing a routing protocols but can introduce high packet delay
» Example: DSR
Geographic routing: find a path based on geographic coordinates
» Does not require any topology information
» Does not maintain forwarding tables
» Example: GPSR

## Slide 8: Proactive or Table-based Protocols
8
Proactive: routers maintain routes independently of the need for communication
» Similar to wired networking – uses forwarding table
Route update messages are sent periodically or when network topology changes
Low latency – forwarding information is always readily available
Bandwidth might get wasted due to periodic updates

## Slide 9: Reactive or On-Demand Routing
10
Routers discover a route only when there is data to be sent
Saves energy and bandwidth during periods of inactivity or low activity
Route discovery introduces significant delay for the first packet of a new transfer
Bad if many nodes send packets to many destinations at random times or in unstable networks

## Slide 10: Ad Hoc Routing
11
Classes: proactive versus reactive routing
Proactive, table based routing: DSDV
Reactive routing DSR
Geographic routing: GPSR

## Slide 11: Packet Forwarding versus Routing
Peter A. Steenkiste
12
Routing finds a path between two end-points
Forwarding receives a packet and decides which egress port to send it out on
Most networks use a routing protocol to pre- calculate paths between every pair of nodes
» Routers put the result in a forwarding table
Forwarding only requires a lookup in the forwarding table – fast!
IP1 | 1
IP2 | 2
IP3 | 2
IP4 | 2
IP5 | 3
Destination Address
Port
1
2
5
3
4
Router
1
3
2

## Slide 12: Generic Router Architecture
Peter A. Steenkiste
13
13
Lookup IP Address
Update Header
Header Processing
Data Hdr
Data
Hdr
1M prefixes
Off-chip DRAM
Address Table
IP Address
Next Hop
Queue Packet
Buffer Memory
Off-chip DRAM

## Slide 13: Traditional Routing Solutions
Background
Link state routing
» Each router obtains a full topology of the network by having nodes periodically flood connectivity information
» Each router then uses Dijkstra’s algorithm to locally calculate its forwarding table
» Bad fit for ad hoc: LS flooding creates a lot of traffic and relies on all routers having a consistent view of network
Distance vector
» Each router tells its neighbors its shortest path to each destination
» Routers then use the “best” option provided to them
» Based on the Bellman-Ford algorithm
» More promising for ad hoc: has lower routing overhead
» Challenge is how to avoid routing loops (details omitted)

## Slide 14: Routes from Node A
Set of shortest paths forms tree
» Shortest path spanning tree
Solution is not unique
» E.g., A-E-F-C-D also has cost 7
A
E
F
C
D
B
Background
2
3
6
4
1
1
1
3
Forwarding Table for A |  | 
Dest | Cost | Next Hop
A | 0 | A
B | 4 | B
C | 6 | E
D | 7 | B
E | 2 | E
F | 5 | E

## Slide 15: Different View: How to Get to Node C
A
E
F
C
D
B
Background
2
3
6
4
1
1
1
3
Forwarding Table for A |  | 
Dest | Cost | Next Hop
C | 6 | E
Forwarding Table for C |  | 
Dest | Cost | Next Hop
C | - | -
Forwarding Table for F |  | 
Dest | Cost | Next Hop
C | 1 | C
Forwarding Table for E |  | 
Dest | Cost | Next Hop
C | 4 | F
Forwarding Table for B |  | 
Dest | Cost | Next Hop
C | 2 | F
Forwarding Table for D |  | 
Dest | Cost | Next Hop
C | 1 | C

## Slide 16: Distance-Vector Method
Router periodically exchanges tables with neighbors
» Contains the cost and next hop of best known path to all destination
Routers pick the best of the candidates paths
» May be the path it is currently using already
A
E
F
C
D
B
2
3
6
4
1
1
1
3
Initial Table for A |  | 
Dest | Cost | Next Hop
A | 0 | A
B | 4 | B
C |  | –
D |  | –
E | 2 | E
F | 6 | F
Background

## Slide 17: Destination-Sequenced Distance Vector (DSDV)
By Perkins and Bhagvat
DV protocol specifically designed for wireless
» Exchange of routing tables
» Routing table: the way to the destination, plus the cost
Each node advertises its presence and tables
» Maintains fresh routes by periodically sending updates to neighbors
» Update for each destination: hop count, sequence number
Uses sequence number to avoid loops
» Advertisements for each destination include sequence number that is incremented for each update
» Since loops are created by advertisements based on old routing information, they can be detected

## Slide 18: DSDV Properties
Keep the simplicity of Distance Vector
Guarantees Loop Freeness
» While adding minimal overhead
Allow fast reaction to topology changes
» Make immediate route advertisement on significant changes in routing table
Drawbacks:
» Overhead can be significant under dynamic conditions and mobility
» Many ad hoc networking scenarios do not require all- all connectivity, so some effort is wasted
Based on: cone.informatik.uni-freiburg.de/teaching/vorlesung/manet-s07/exercises/DSDV.ppt

## Slide 19: Overview
20
Ad hoc networking concept
Proactive versus reactive routing
Proactive, table based routing: DSDV
Reactive routing DSR
Geographic routing: GPSR
Wireless link metrics
Ad hoc networking examples

## Slide 20: Dynamic Source Routing (DSR) Key Features
On-demand route discovery finds route only when it is needed
» Avoid overhead of periodic route advertisements
Uses source routing: path information is stored in the packet header
DSR control functions:
» Route discovery: senders obtain route to destination
» Route maintenance: detect changes in topology and update routes that are affected
» Route caching: nodes cache route information to avoid route discovery for every packet
Caching can be done on sender and intermediate routers
Flush broken routes from cache
Hop 1
Hop 1
… Dest

## Slide 21: DSR Route Discovery
Source broadcasts a route-request towards the destination
» The request includes a (partial) path from source to destination
Each node forwards the request by adding own address to the path and re-broadcasting
Requests propagate outward until:
» The destination is found, or
» A node that has a route to the destination is found

## Slide 22: Route Request is Re-Broadcasted until Destination is Reached
A
Source C
G
H
E
D
B
Route Request
Destination F
C C,G,H,F
F C,G
F C,G,H

## Slide 23: C Transmits a Packet to F
A
Source
C
G
H
Destination F
E
D
B
F
H,F
G,H,F

## Slide 24: Forwarding Route Requests
A request is forwarded by a node if:
» Node is not the destination
» Node not already listed in recorded source route
» Node has not seen request with same sequence number
» IP TTL field may be used to limit scope
Destination copies selected route into a Route-reply packet and sends it back to Source
» I.e., route reply uses reverse path of the route selected by the destination
» Destination can choose one of the paths, e.g., first path (with shortest delay)

## Slide 25: Route Cache
All source routes learned by a node are kept in a Route Cache
» Routes are learned by overhearing route requests/responses
» Reduces cost of route discovery
If an intermediate node receives a route request for a destination and has an entry for the destination in its route cache, it
» Responds to the request using the cached information
» Does not propagate the request any further
Nodes use their local route cache when asked to send a data packet
» If route is missing, they initiate a route request

## Slide 26: Basic Route Maintenance
When forwarding a packet, each sender must get an acknowledgement from the next hop
» Will retransmit the packet up to a limit if needed
If no ACK is received it drops the packet and notifies the sender A of the broken link
A removes the route from its route cache and ..
» Intermediate nodes also remove any cached entries to E
Will do a new route discovery when it sends another packet to E
» It is left up to TCP to recover from the packet loss
A
B
C
D
E

## Slide 27: Discussion
Source routing is good for certain types of networks and traffic loads
» For example, stable traffic flows and/or a small number of sender-receiver pairs
» Stable network topologies, e.g., with limited mobility
Periodic messages are avoided
Significant delay for the first packet to a destination
» Also, need to buffer packets

## Slide 28: Overview
Ad hoc networking concept
Proactive versus reactive routing
Proactive, table based routing: DSDV
Reactive routing DSR
Geographic routing: GPSR
Wireless link metrics
Ad hoc networking examples

## Slide 29: Greedy Perimeter Stateless Routing (GPSR)
30
Use positions of neighboring nodes and packet destination to forward packets
  No connectivity or global topology is assumed
– no forwarding or path information anywhere!
  Nodes are assumed to know their location
  Need a mechanism for address-to-location look up
Two forwarding techniques is used
  Greedy forwarding, if possible
  Perimeter forwarding, otherwise

## Slide 30: GPSR – Greedy forwarding
A sender/forwarder x chooses to forward to a neighbor y such that {dxy + dyD} is minimum
x
y
D
31

## Slide 31: GPSR – Perimeter forwarding
Peter A. Steenkiste
32
What happens if a node does not have a neighbor that is closer to the destination?
Right Hand Rule: you forward the packet to your first neighbor clockwise around yourself
  Traverse an interior region in clockwise edge order
  Guaranteed to reach a (reachable) destination for planar graph
D
z
y
v
w
VOID
x
This sequence of edges traversed is called a PERIMETER

## Slide 32: Discussion
Many variants:
» Hybrid approaches mix different solutions
» Hierarchical: create a hierarchy of clusters
Many proposals for optimizations
» Links use different frequencies, multiple radios, etc.
» Link metrics that consider interference level, …
Best solutions is highly context dependent: density, traffic load, degree of mobility, …
Practical applications are rare by exist:
» Mesh networking: wireless, last mile Internet access
» Challenging conditions: first responders, military, ..
» In the future maybe vehicular, drones, …

## Slide 33: Summary
Ad hoc networks face many challenges
» Bad links, interference, mobility, …
» Makes routing very challenging
» Limited support: hardware and driver limitations
Many proposals!
» Proactive routing: variants of “wired” routing protocols
» Reactive routing: only establish a path when it is needed
» Geographic routing: use destination location info only
» Many variants and extensions
Specific challenges depend on the application domains
» Mesh versus vehicular
» Active area of research

## Slide 34: Some References
DSR:
» www.cs.rice.edu/~dbj/pubs/aw-dsr.pdf
DSDV:
» www.cs.jhu.edu/~cs647/class-papers/Routing/p234-perkins.pdf
GPSR:
» www.eecs.harvard.edu/~htk/publication/2000-mobi-karp-kung.pdf
ETX:
» pdos.csail.mit.edu/papers/grid:mobicom03/paper.pdf
ETT
» http://www.cs.jhu.edu/~cs647/class-papers/Routing/p114-draves.pdf