## Slide 1
CSCE 5520
Wireless Networks and Protocols Lecture 1: Wireless Introduction
Asif I Baba
University of North Texas
Many slides adapted form Peter Steenkiste lectures at
Carnegie Mellon University

## Slide 2: Where to Look for Things
LMS (canvas)
» Lecture schedule and slides
» Office hours, contact information, …
» Deadlines for homeworks, surveys, and projects
» Handouts
Canvas is used for any course information, announcements, and handouts

## Slide 3: Textbook and Readings
Textbook” "Wireless Communication Networks and Systems", Corry Beard and William Stallings, Pearson, 2015
» Best fit for the course
The course is not based on the book
» The book should be used to read about the topics covered in class, e.g., to clarify points or get more depth
» Book does not cover all material, but slides are detailed
Some additional readings will be uploaded to canvas

## Slide 4: Collaboration
Traditional rules of collaboration apply
» https://vpaa.unt.edu/ss/integrity
You must complete individual assignments and tests by yourself
You are expected to collaborate with your partner in the team-based projects (if any)
It is acceptable and encouraged to help fellow students with generic problems
» e.g. where to find documentation, use of tools, ..
» You must give proper credit when reusing material

## Slide 5: Networks are everywhere!
Almost all areas of computing are network-based
  Distributed computing
  Big Data
  Cloud Computing
  Internet of Things
  Smart Cities

## Slide 6: Networking is Fueling All Sectors of Economy
Networking companies are among the most valued companies: Apple, AT&T, Samsung, Verizon, Microsoft, China Mobile, Alphabet, Comcast, NTT, IBM, Intel, Cisco, Amazon, META (Facebook), …
Note: Apple became highly valued only after it switched from computing to communications (iPhone)

## Slide 7: Networking is Fueling All Sectors of Economy
Wi-Fi provides significant benefits to economies worldwide. The global economic value of Wi-Fi is estimated at more than $3.5 trillion USD. By 2025 that value is expected to grow to nearly $5 trillion.
5G is poised to generate up to $1.5 trillion in additional GDP in the U.S. between 2021 and 2025, according to a new economic study by Accenture, commissioned by Qualcomm.
https://www.wi-fi.org/discover-wi-fi/value-wi-fi
https://www.axios.com/sponsored/content-item/qualcomm-how-5g-will-become-the-underlying-foundation-of-the-u-s-economy

## Slide 8: Mobility vs Wireless
Mobile vs. stationary
Wireless vs. wired

## Slide 9: Wireless Networking
Impact of Wireless on Networking:
  Not tied to walls/infrastructure
    Ad-hoc networks
  Error-prone
    Traffic management
  Frequent Disconnections
    Resource management
    Quality of service for multimedia
  Battery operate
    Media access and networking while sleep
  Broadcasting
    security

## Slide 10: Mobile Networking
Impact of mobility on Networking:
  Location
  Addressing
  Handoff

## Slide 11: Why Wireless networks?
Wireless (WiFi) is ubiquitous.
Most of the access (end user connectivity) is wireless
  Smart phones, Tablets, and many laptops (Ultrabooks) have no wired Ethernet connections
Most of telecommunication carriers’ revenue is in wireless
New Developments:
  5G: 1 Gbps Metropolitan Area Networks
  Vehicular Networking (802.11p)
  Cognitive networks: Sharing unused spectrum

## Slide 12: Mobile Internet
Over 55% of website traffic comes from mobile devices.
92.3% of internet users access the internet using a mobile phone.
There are approximately 4.32 billion active mobile internet users.
Africa has the highest proportion of internet traffic from mobile devices - 69.13%.
There will be over 1 billion 5G connections worldwide by 2025.

## Slide 13
USA: 2025 Mobile Economy Forecast
USA is the second-largest market for 5G and IoT technology. The three major operators in the market (AT&T, Verizon, and T-Mobile) have made partnerships with vendors to expand their 5G technologies.

## Slide 14: Internet of Things

## Slide 16: Wireless Communication
Transmitting voice and data using electromagnetic waves in open space
Electromagnetic waves
  Travel at speed of light (c = 3x108 m/s)
  Has a frequency (f) and wavelength (l)
    c = f x l
  Higher frequency means higher energy photons
  The higher the energy photon the more penetrating is the radiation

## Slide 17: Electromagnetic Spectrum
104
102
100
10-2
10-4
10-6
10-8
10-10
10-12
10-14
10-16
104
106
108
1010
1012
1014
1016
1018
1020
1022
1024
IR
UV
X-Rays
Cosmic
Rays
Radio
Spectrum
1MHz ==100m 100MHz ==1m
10GHz ==1cm
< 30 KHz VLF 30-300KHz LF
300KHz – 3MHz MF 3 MHz – 30MHz HF 30MHz – 300MHz VHF
300 MHz – 3GHz UHF
3-30GHz SHF
> 30 GHz EHF
Micro wave
Visible light

## Slide 18: Spectrum Shared by Many Users
Spectrum allocated by FCC and NTIA
Two types of spectrum bands:
  Licensed spectrum: exclusive access to an organization
    Federal agencies, broadcast TV, first responders, …
    Commercial, e.g., cellular operators
  Unlicensed spectrum: everyone can use it with appropriate equipment, e.g., WiFi, zigbee, …
Other trends:
» Technology improvements have allowed us to use higher frequency bands over time
» Many bands have low utilization
» Older bands often use very inefficient technologies

## Slide 19: Wireless Technologies
1960 1970
1950
1980
1990
2000
2010
3 MHz
30 MHz
300 MHz
3 GHz
30 GHz
300 GHz
3 THz
VHF
IR
SHF
HF
EHF
UHF
Shortwave radio
1930 1940
Black-and
White TV
FM radio
Mobile Two-way
radio
Color TV
Cordless phone
Terrestrial
microwave Experimental
Communications satellite
Communications
satellite
Infrared Wireless LAN
Optical Communications satellite
Wi-Fi
WiMAX/LTE
Ultra- wideband
ZigBee
Cellular phone

## Slide 20: Why so many Technologies?
Peter A. Steenkiste. CMU
Technologies have different
» Signal penetration
» Frequency use
» Cost
» Market size
Throughput (Mbps)
Diverse application requirements
» Energy consumption
» Range
» Bandwidth
» Mobility
» Cost
100
1m
10m 100m 1Km
Range
10km 100km
1
10
WiMAX/LTE
» Age, integration
UWB
BT
Zigbee
WiFi
IrDA
Diverse deployments
» Licensed versus unlicensed
» Provisioned or not

## Slide 21: Application Trends in Wireless
Early days: specialized applications
» Broadcast TV and radio, voice calls, data, ..
» Holds for wireless and wired
Today: flexible wireless platforms
» Phones, tables, and laptops all run similar applications
» Same trend as for wired networks: everything runs over the Internet
Wireless is expanding in new domains
» Sensor networks, body area networks, …
» Edge of the internet is increasingly wireless
» Many of these applications are unique to wireless
Future?

## Slide 22: Scope of Wireless Covered in the Course
Significant depth on two technologies:
» Wireless in unlicensed band: WiFi
» Wireless in licensed spectrum: cellular
» Focus is on optimizing performance with limited spectrum
» Sophisticated protocols to fight challenging physical layer
Other wireless communication technologies
» RFID/NFC, low-power, sensor networks, …
Wireless deployments
» Infrastructure WiFi, ad hoc, sensor networks, vehicular, ..
Other applications of wireless
» GPS, Wifi for localization, dynamic spectrum access, …
» Other topics covered in the surveys

## Slide 23: Some History…
Hertz discovered electromagnetic waves (1880)
Tesla credited with first radio communication in 1893
Wireless telegraph invented by Guglielmo Marconi in 1896
First telegraphic signal traveled across the Atlantic ocean in 1901
First “cell phone” concept developed in 1946
» FCC allocated spectrum in the 70s; commercial service in the early 80s
» Data started only in the 90s
GPS project started in 1973, complete in 1995
WiFi technology developed in the mid-1990s

## Slide 24: The MTS network
http://www.privateline.com/PCS/images/SaintLouis2.gif

## Slide 25: The origin of mobile phone
America’s mobile phone age started in 1946 with MTS
First mobile phones bulky, expensive and hardly portable, let alone mobile
» Phones weighed 40 Kg~
Operator assisted with 250 maximum users

## Slide 26: Short History of WiFi
In 1985, the FCC opened up the 900 Mhz, 2.4 GHz and 5.8 Ghz bands for unlicensed devices
NCR and AT&T developed a WiFi predecessor called “Wavelan” starting in 1988
» NCR wanted to connect cashier registers wirelessly
» Originally used the 900 MHz band and ran at 1 Mbps
Standardization started in early 90s and led to 802.11b (1999) and 802.11a (2000)
» Pre-standard products were available earlier
Today –many standards!
» Working on 802.11ax and ay - rates up to several Gps
» Very sophisticated: OFDM, MIMO, multi-user MIMO, ..
» Multiple frequency bands: 2.4 GHz, 5 GHz, 60 GHz

## Slide 27: Early WiFi Interfaces
PCMCIA form factor made Wavelan more portable
Wavelan at 900MHz 1 Mbps throughput

## Slide 28: Hype Cycle for Enterprise Networking and Communications, 2018

## Slide 31: Outline
Goals and structure of the course
Administrative stuff
A bit of history
Wireless technologies
Building a network
» What pieces do we need
» The OSI model
» Packet-based communication
» Challenges in Wireless Networking

## Slide 32: The Internet is Big and Has Many, Many Pieces
Application
Protocol Software
Links
Router Hardware
Router Software (many protocols)
Bridge HW/SW
Application
Operating System
Operating System
Computer
Network Interface
Computer
How do you design something this complex?

## Slide 33: What Pieces Do We Need?
We need to be able to send bits
» Over wired and wireless links
» Based on analog signals
We really want to send packets
» Statistical multiplexing: users can share link
» Need addresses to deliver packets correctly
But network may not be reliable
» Bit errors, lost packets, …
» Must recover from these errors end-to-end
You need applications and services
» Otherwise: who cares?
Module:
Physical
Datalink Network
Transport
Application

## Slide 34: Hosts Exchanging Packets can be Easy or Hard
Two or more hosts talk over a wire (bits)
Groups of hosts can talk at two levels
» Hosts talk in a network is homogeneous in terms of administration and technology
» Hosts talk across networks that have different administrators and technologies
Differ in physical and admin properties, scale
Internet
Physical
Datalink Internet
Scaling up

## Slide 35: A Bit More Detail
Physical layer delivers bits between the two endpoints of a “link”
» Copper, fiber, wireless, visible light, …
Datalink layer delivers packets between two hosts in a local area network
» Ethernet, WiFi, cellular, …
» Best effort service: should expect a modest loss rate
» “Boxes” that connect links are called bridges or switches
Network layer connects multiple networks
» The Inter-net protocol (IP)
» Also offers best effort service
» Boxes that forward packets are called routers
Scaling up the network

## Slide 36: Our Internet So Far
The Internet as five modules that are stacked as a set of layers
» More on this later
Five layers is nice, but …
» Each module is still huge!
» What about communication?
We need protocols!
Protocol modules within each layer on different devices allow the devices communicate
Application
Inter-network
Datalink
Physical
Transport

## Slide 37: Protocol Enable Communication
An agreement between parties on how communication should take place.
Protocols must define many aspects of the communication.
Syntax:
» Data encoding, language, etc.
Semantics:
» Error handling, termination, ordering of requests, etc.
Protocols at hardware, software,
all levels!
Example: Buying airline ticket by typing.
Syntax: English, ascii, lines delimited by “\n”
Friendly greeting
Muttered reply
Get to Heinz Hall?
That way …
Thank you

## Slide 38: Protocol and Service Levels
Application
Transport
Inter-network Datalink
Physical
Host
Host
LAN
Internet
LAN

## Slide 39: The ISO Layered Network Model
The Open Systems Interconnection (OSI) Model.
Application
Presentation
Session
Transport
Network
Data link
Physical
7
6
5
4
3
2
1
Network
Data link
Physical
Application
Presentation
Session
Transport
Network
Data link
Physical

## Slide 40: OSI Functions
(1) Physical: transmission of a bit stream.
(2) Data link: flow control, framing, error detection.
(3) Network: switching and routing.
(4) Transport: reliable end to end delivery.
(5) Session: managing logical connections.
(6) Presentation: data transformations.
(7) Application: specific uses, e.g. mail, file transfer, telnet, network management.

## Slide 41: Life of Packet
Peter A. Steenkiste. CMU
Bridge/Switch
Router/Gateway
Host
Host
Application
Presentation Session Transport Network
Data Link Physical

## Slide 42: A TCP / IP / 802.11 Packet
Preamble MAC header
LLC / SNAP header
IP header
TCP header
Data
Application
Presentation
Session
Transport
Network
Data link
Physical

## Slide 43: Example: Sending a Web Page
Http hdr Web page
TCP
header
. . .
Application payload
Application
Presentation
Session
Transport
Network
Data link
Physical

## Slide 44: OSI Motivation
Standard approach of breaking up a system in a set of components with well defined interfaces, but components are organized as a set of layers.
» Only horizontal and vertical communication
» Components/layers can be implemented and modified in isolation without affecting the other components
Each layer offers a service to the higher layer, using the services of the lower layer.
“Peer” layers on different systems communicate via a protocol.
» higher level protocols (e.g. TCP/IP, Appletalk) can run on multiple lower layers
» multiple higher level protocols can share a single physical network

## Slide 45: Benefits of Layered Architecture
easily as long as its interfaces are respected
» Does not impact the other components in the system
» Different implementation versus different protocols
In practice: most significant evolution and diversity at the top and bottom:
» Applications: web, peer-to-peer, video streaming, ..
» Physical layers: optical, wireless, new types of copper
» Only the Internet Protocol in the “middle” layer
Significantly reduces the complexity of building and maintaining the system.
» Effort is 7 x N instead of N7 for N versions per layer
The implementation of a layer can be replaced True
For
Wireless?

## Slide 46: Impact of the Physical Layer
Wires:
reliable and predictable
Application Transport Inter-network Datalink
Physical
Wireless:
error prone and variable
Packet losses and variable delay and bandwidth
Disconnections
Mobility: IP addresses change
Must manage complex PHY to perform error control
Sophisticated modulation & coding, bit rate adaptation