## Slide 1
1
CSCE 5520
Wireless Networks and Protocols Localization
Page 1

## Slide 2: Outline
2
Properties of localization procedures
Approaches
» Proximity
» Trilateration and triangulation (GPS)
» Finger printing (RADAR)
» Hybrid systems
Page 2

## Slide 3: Properties of localization procedures
3
Physical position vs data types
Reference systems
Processing: localized vs centralized
Data quality
» Accuracy and precision
» Scale
Deployment aspects
» Limitations
» Cost
→ Very diverse systems – lots of research
Page 3

## Slide 4: Data types
4
Point locations in terms of coordinates:
» physical or geometric locations
» GPS: latitude and longitude, height
» Cartesian coordinate system based on three orthogonal planes
Extended region locations given by names:
» symbolic locations
» CMU, Wean Hall, room 8202
Page 4

## Slide 5: Location-awareness
5
Location model: data structure that organizes locations
Location-based routing
» symbolic location model
» geometric location model
» hybrid location model
Examples
» symbolic location model: address hierarchy DH.Floor2.2105
» geometric location model: GPS coordinate (12.3456°N, 123.456°E)
» hybrid location model: combination of address and coordinate DH.Floor2.2105.Seat(0,4)
Page 5

## Slide 6: Quality of Position Information
Peter A. Steenkiste, CMU
6
Precision:
the ratio with which a given accuracy is reached, averaged over many repeated attempts
Example:
average error of less than 20cm
in 95% of cases
Positioning accuracy:
largest distance between an estimated position and the true position
Only pairs of precision and accuracy make sense
Page 6

## Slide 7: Precision vs. Accuary
Peter A. Steenkiste, CMU
7
https://www.sophia.org/tutorials/accuracy-and-precision--3
Page 7

## Slide 8: Approaches
Peter A. Steenkiste, CMU
8
Proximity: estimate distance between two nodes
Trilateration and triangulation
» using elementary trigonometric properties: a triangle is completely determined,
  if two angles and a side length are known
  if the lengths of all three sides are known
» infer a 3d position from information about two triangles
Fingerprinting (scene analysis)
» using radio characteristics as fingerprint to identify it
Hybrid methods: multiple sources of information
Page 8

## Slide 9: Proximity and Distance
Peter A. Steenkiste, CMU
9
Binary nearness: using finite range of wireless communication and/or threshold
» within range of a beacon signal from a source with known position
» yields region locations, e.g.: cell in cellular network
Distance measurement (ranging)
» Received signal strength
» Time of flight (time of arrival)
» Time difference of arrival
Page 9

## Slide 10: Measuring Location: Trigonometry Basics
Peter A. Steenkiste, CMU
10
Triangles in a plane
» Lateration: distance measurement to known reference points
  a triangle is fully determined by the length of its sides
  Time of Flight (e.g. GPS, Active Bat)
  Attenuation (e.g. RSSI)
» Angulation: measuring the angle with respect to two known reference points and a reference direction or a third point
  a triangle is fully determined by two angles and one side as shown
  Phased antenna arrays
  aircraft navigation (VOR)
Page 10

## Slide 11: Trilateration
Peter A. Steenkiste, CMU
11
http://gpsworld.com/innovation-where-are-we/
Page 11

## Slide 12: Mathematical Background
Peter A. Steenkiste, CMU
13
Computing positions between three known positions (xi, yi) and an unknown position (xu, yu) given distances ri btw (xi, yi) and (xu, yu)
Yields three equations (xi-xu)2 + (yi-yu)2 = ri2
Linear equations by subtracting 3rd from 1st and 2nd: quadratic terms xu2 and yu2 disappear
» 2(x3 – x1)xu + 2(y3 – y1)yu = (r 2 – r 2) - (x 2 – x 2) - (y 2 – y 2)
1 3 1 3 1 3
2 3 2 3 2 3
» 2(x3 – x2)xu + 2(y3 – y2)yu = (r 2 – r 2) - (x 2 – x 2) - (y 2 – y 2)
In 3D: yields two points
Positioning with imprecise information:
» Add redundancy: over determined solution
» Least squares estimates

## Slide 13: GPS
Peter A. Steenkiste, CMU
Radio-based navigation system developed by DoD
» Initial operation in 1993
» Fully operational in 1995
System is called NAVSTAR
» NAVigation with Satellite Timing And Ranging
» Referred to as GPS
» Has been improved over time
Series of 24 (now 32) satellites, in 6 orbital planes
Works anywhere in the world, 24 hours a day, in all weather conditions and provides:
» Location or positional fix
» Velocity, direction of travel
» Accurate time
www.fws.gov/southeast/gis/training_2k5/GPS_overview_APR_04.ppt 14

## Slide 14: GPS Constellation
Peter A. Steenkiste, CMU
15
24 satellites are needed to guarantee that 4 are always visible everywhere
Extra satellites provide redundancy
» Deal with maintenance, replacement, …
https://www.colorado.edu/geography/gcraft/notes/gps/gps_f.html

## Slide 15: GPS involves 5 Basic Steps
Peter A. Steenkiste, CMU
16
Satellite Ranging
» Determining distance from satellite
Trilateration
» Intersection of spheres
Timing
» Why consistent, accurate clocks are required
Positioning
» Knowing where satellite is in space
Correction of errors
» Correcting for ionospheric and tropospheric delays

## Slide 16: How GPS works?
Peter A. Steenkiste, CMU
17
Range from each satellite calculated
range = time delay X speed of light
Technique called trilateration is used to determine your position or “fix”
» Intersection of spheres as described earlier
At least 3 satellites required for 2D fix
However, 4 satellites are used
» The 4th satellite used to calculate drift of clock in GPS receivers relative to that of the satellites
» Yields much better accuracy and provides 3D fix

## Slide 17: Satellite Positions
Peter A. Steenkiste, CMU
18
Each satellite has an atomic clock that keeps time very accurately
» Satellites synchronize their clocks
» Also periodically synchronize with the true time maintained on earth
Satellites also know their location very accurately

## Slide 18: Determining Range
Peter A. Steenkiste, CMU
Measure time difference between the same part of code
From satellite
From r
Each satellite periodically generates a pseudo random code
» Receivers also locally generate the codes in synchronized fashion
Receivers measure Time of Arrival (TOA) of codes
Transmission includes Time of Transmission (TOT) of code and the location of the satellite at that time
» Allows receiver to calculate Time of Flight and distance
Series of ones
and zeroes repeating every 1023 bits. So Complicated alternation
led
 |  |  |  |  |  |  |  |  |  | of bits that pattern looks random thus cal “pseudorandom code”. |  |  |  |  |  |  |  |  |  |  |  |  |  | 
eceiver |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | 19 |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 19: Three Satellite Ranges Known
21
20,000 Km radius
22,000 Km radius
21,000 Km radius
Located at one of these 2 points.
However, one point can easily
be eliminated because it is either
not on earth or moving at impossible rate of speed.
Peter A. Steenkiste, CMU

## Slide 20: Accurate Timing is the Key
Peter A. Steenkiste, CMU
22
Satellites have very accurate atomic clocks
Receivers have less accurate clocks
Measurements made in nanoseconds
» Speed of light (c) ~ 1 ft/nanosecond
1/100th of a second error could introduce error of 1,860 miles
Discrepancy between the satellite clock and the receiver clocks must be resolved
Fourth satellite is used to solve the 4 unknowns (X, Y, Z and receiver clock error)
Page 20

## Slide 21: Satellite Positioning
Peter A. Steenkiste, CMU
23
Required in the equation to solve the 4 unknowns is the actual location of the satellite.
» 3 coordinates for location, plus clock drift of receiver relative to the satellite clocks
Satellites are in relatively stable orbits and constantly monitored on the ground
Satellite’s position is broadcast in the “ephemeris” data streamed down to receiver
» Downloading complete set of almanac data requires 12.5 minutes (transmitted at 50 bps)

## Slide 22: Sources of Errors
Peter A. Steenkiste, CMU
24
Largest source is due to the atmosphere
» Atmospheric refraction
– Charged particles
– Water vapor
Other sources:
» Geometry of satellite positions
» Multi-path errors
» Satellite clock errors
» Satellite position or “ephemeris” errors
» Quality of GPS receiver
Ionosphere (Charged Particles)
Troposphere

## Slide 23: How about Indoors?
Peter A. Steenkiste, CMU
25
We can use received WiFI signal strength (RSS) to measure distance to APs with known location!
Does not work in practice: too many factors affects RSS: objects, people, …
» Triangulation based on RSS tends to results tend to give large, unpredictable errors
How about using time of arrival?
» E.g., based on sound, radar-like techniques, …
» Works better, but it is still hard
» Can work well but often requires special infrastructure
» Reflections can also create inaccuracies: longer path!

## Slide 24: CAESAR: Carrier Sense-based Ranging
Peter A. Steenkiste, CMU
26
Question: can we use time of flight ranging using commodity WiFi hardware?
Yes, but it gets a bit messy
» Need to include SNR measurement
Local station determines location of (mobile) remote stations
Design criteria
» Exploit standard 802.11 protocol implementations
» Real time results
» Low cost (low network usage, no additional hardware, minimal calibration)

## Slide 25
CAESAR: Key Idea Time of flight from ACKs Speed of light: c = ~300m/s WLAN clock 44MHz  Resolution: 300/(2*44) = 3.4m Distance d = c*(tMacIdle-tSIFS-tFD)/2 1 2 | 
Distance = ½ time from end of data to beginning of ACK | 
Peter A. Steenkiste, CMU 27 | 

## Slide 26: CAESAR: Adjustment to Noise
Peter A. Steenkiste, CMU
28
Method depends on correct estimation of response time, which depends on the SNR
Automatic gain control is used if
» Preferred region (PR): no AGC
» Strong signal detected (SSD): e.g. subtract 30dB from from signal
» Weak signal detected (WSD): may need adjust signal to to bring it into PR (or signal is not detected)
Proposed solution:
» Detect states SSD, WSD, and preferred range
» Use different values for Time for Frame Detection ( tFD)

## Slide 27: Outline
Peter A. Steenkiste, CMU
29
Properties of localization procedures
Approaches
» Proximity
» Trilateration and triangulation (GPS)
» Finger printing (RADAR)
» Hybrid systems

## Slide 28: Angle of Arrival (AoA)
Peter A. Steenkiste, CMU
30
A measures the direction of the incoming signal using a radio array.
By using 2 anchors, A can determine its position
Alternatively: the anchor measure the angle of A’s signal and coordinate

## Slide 29: Angle of Arrival Techniques
Peter A. Steenkiste, CMU
31
Antenna arrays are increasingly popular
They are usually used to steer the signal, but can be used to identify the angle at which it arrives
Difference in arrival time can be used to measure angle
t1
t2

## Slide 30: Outline
Peter A. Steenkiste, CMU
32
Properties of localization procedures
Approaches
» Proximity
» Trilateration and triangulation (GPS)
» Finger printing (RADAR)
» Hybrid systems
Page 30

## Slide 31: Location Fingerprinting
Peter A. Steenkiste, CMU
33
Fingerprint Methods for Recognizing Locations
» Examples
  Visual identification of places from photos
  Recognition of horizon shapes
  Measurement of signal strengths of nearby networks (e.g. RADAR)
» Method: computing the difference between a feature set extracted measurements with a feature database
» Advantages: passive observation only (protect privacy, prevent communication overhead)
» Disadvantage: access to feature database needed

## Slide 32: RADAR: Key Idea
Peter A. Steenkiste, CMU
34
RSS from multiple APs tends to be unique to a location
0
20
40
60
80
100
Distance along walk (meters)
AP1
AP2 AP3

## Slide 33: RADAR Approach
Peter A. Steenkiste, CMU
35
Scenario: floor layout with three base stations (in the hallways)
Empirical method
» offline phase: database is constructed
  collect signal strength measurements from all three base stations at 70 distinct locations
  store each of the 70 measurement triples together with the spatial location and orientation in a database
» online phase: position can be determined
  measure the current signal strength from all three base stations
  find the most similar triple(s) in the database
» Resolution 2.94m (50th percentile)
- Base Station

## Slide 34: Model-Based Radio Map
Peter A. Steenkiste, CMU
36
Model set-up phase has high cost
Alternative use radio propagation model and floor plan (instead of measurements)
» Considered models
  Rayleigh fading model: small-scale rapid amplitude fluctuation to model multi-path fading
  Rician distribution model: like Rayleigh but with additional LoS component
  Floor Attenuation Factor propagation model: large scale path loss with building models
  Wall Attenuation Factor model: considers effects from walls between transmitter and receiver
» Resolution 4.3m (50th percentile)

## Slide 35: Effects of applying correction
Peter A. Steenkiste, CMU
37
with correction for walls
signal strength as a function of distance

## Slide 36: Limits of Localization Using Signal Strength
Peter A. Steenkiste, CMU
38
Measuring distance based on signal strength is an attractive idea for wireless sensor networks:
» RSS does not require additional hardware
» RSS declines with distance
» Many different promising methods proposed
But accuracy is quite limited
» 802.11 technology with a range of methods and environments tested
» Median localization error of 10ft and 97th percentile of 30ft
Many technologies with higher accuracy have been developed
» E.g., UWB, use of AoA, …

## Slide 37: Hybrid Technologies
Peter A. Steenkiste, CMU
39
Cell phones: have many other sensors
» Accelerometer, compass, …
Can be used to estimate the user’s walking speed, direction, …
This information can be combined with finger printing based techniques
Especially useful if finger printing provides accurate location in specific points
» When entering a store, escalator, elevators
» Can use the other sensors starting with these well- knownlocations

## Slide 38: Literature
Peter A. Steenkiste, CMU
40
H. Karl and A. Willig (2005). Protocols and Architectures for Wireless Sensor Networks, Ch. 9 Localization and positioning. John Wiley & Sons.
P. Bahl and V. N. Padmanabhan (2000). RADAR: An In- Building RF-based User Location and Tracking System. IEEE INFOCOM 2000, pp. 775-784.
E. Elnahrawy et al. (2004). The limits of localization using signal strength: a comparative study. IEEE SECON 2004, pp. 406-414 .
D. Giustiniano, and S. Mangold (2011). CAESAR: Carrier Sense-Based Ranging in Off-The-Shelf 802.11 Wireless LAN. ACM CoNEXT 2011.